## Slide 1: On Attack Causality in Internet-Connected Cellular Networks
Presented by EunYoung Jeong

## Slide 2: What’s new?
2G GSM
  Only voice call, SMS service
2.5G GSM
  GPRS: General Packet Radio Service
  Introduce data service on GSM network.
  Enables mobile devices to be connected to the Internet.
  Divide CCH (Control Channel) of GSM network to provide data delivery.
    Control signal, SMS, and data service over CCH

## Slide 3: GPRS/EDGE Architecture

## Slide 4: Authentication/Registration
After PDP context setup, mobile device can exchange packets.
GPRS attach
Home Location Register:
User location, availability, services
Packet Data Protocol (PDP) context:
IP address, billing, …

## Slide 5: Packet Arrival

## Slide 6: Receiving device status
To save power, mobile devices are not constantly listening for incoming packets.
States of devices
IDLE
READY
STANDBY
GPRS attach
READY expire
Paging Request
GPRS detach
STANDBY expire
Notes:   IDLE: The device is unregistered and unavailable.
  STANDBY: The device is in power-saving state and periodically listening for “wake up” messages (pages).
  READY: The device is listening for packets.

## Slide 7: Packet Arrival
Notes: SGSN creates paging messages to be sent from a number of base stations.

## Slide 8: Packet Arrival
Paging request
Notes: SGSN creates paging messages to be sent from a number of base stations.

## Slide 9: Paging Procedure
Packet Paging Request
Packet Paging Channel (PPCH)
Packet Channel Response
Packet Random Access Channel (PRACH)
Packet Resource Assignment
Packet Access Grant Channel (PAGCH)
Packet Paging Response
Packet Associated Control Channel (PACCH)
Packet Data Transfer
Packet Data Traffic Channels (PDTCHs)
Notes: Shared control channel among voice and data.
Base station transmits paging request to multiple sectors.
The paging process requires multiple iterations.
When target device becomes awake and hears it, it responds to PRACH (Packet Random Access Channel).
After PDTCH (Packet Data Traffic Channel) assigned, it can receive packet.

## Slide 10: Packet Multiplexing
GPRS multiplex multiple traffic flows to serve large number of users on a single physical channel concurrently.
8 time slots -> a frame
52 frames -> multiframe
Notes: Why do this?
There was only Traffic channel (TCH) and Control Channel (CCH) on GSM.
They have to share single physical channel between voice and data service.

## Slide 11: GPRS Channel Structure
PPCH
PDTCH
Notes: Multiframe is subdivided into 12, four timeslot blocks.
Logical channels mapped onto each block.

## Slide 12: Optimizations
As paging is expensive, paging for every packet is impossible.
  Paging a device takes over 5 seconds.
End devices continue listening to PDTCH for a number of seconds before returning to STANDBY.
  Typically 5 seconds (same as paging overhead)
For this, GPRS differentiates packets at the MAC layer by Temporary Block flows (TBFs) and they are identified by 5-bit Temporary Flow IDs (TFIs).

## Slide 13: Exploiting Connection Teardown
TFIs are implemented as 5-bit fields.
  There can be maximum 32 concurrent flows for each sector.
If an adversary send a message to a phone once every 5 seconds before returning to STANDBY, the targeted device maintains its TFI.
An adversary can block legitimate flows by sending 32 messages to each sector every 5 seconds.

## Slide 14: Exploiting Connection Teardown (Cont.)
55 sectors on Manhattan
32 messages for each sector
41 bytes for each packet (TCP/IP header + 1 byte)
Every 5 second
An adversary can deny service with only 110 Kbps traffic.

## Slide 15: Exploiting Connection Setup
PRACH (or RACH) channel is shared by all hosts attempting to establish connection.
  Slotted-ALOHA protocol is used to minimize contention.
  The maximum theoretical utilization is 0.368.
  Potential system bottleneck.
Given a large number of paging requests,
  RACH becomes very busy.
  Many of connection requests may fail.
  It blocks voice connection as well as data connection.

## Slide 16: Teardown Attack Simulation
Target
  Manhattan cellular data service
  Exhaust TFIs of data service with malicious traffic
Legitimate traffic
  Modeled as Poisson random process
  Voice calls: 50,000 per hour (120 seconds duration)
  Data calls: 20,000 per hour (10 seconds duration)
Attack flows
  Modeled by Poisson random process
  100 - 200 Kbps

## Slide 17: Teardown Attack
At rate > 160 Kbps, the cellular data service within Manhattan is virtually nonexistent.
Voice channel is not affected. (separate use of channel)
At 200 Kbps

## Slide 18: Setup Attack Simulation
Target
  Manhattan cellular voice and data service
  Exhaust RACH channel that is shared by voice and data
Legitimate traffic
  Modeled as Poisson random process
  Voice calls: 50,000 per hour (120 seconds duration)
  Data calls: 20,000 per hour (10 seconds duration)
Attack flows
  Modeled by Poisson random process
  2200 – 4950 Kbps

## Slide 19: Teardown Attack
Both voice and data flows experience blocking on the RACH.
The dual use of control channel allows interference.
At 4950 Kbps

## Slide 20: Possible Mitigation
Adding more range of TFI values
  32 concurrent flow/sector is requisite concession.
  Increasing it will degrade individual connectivity.
Adding more bandwidth
  High cost of connection establishment is same.
  Effect of adding bandwidth is limited.

## Slide 21: Failure of Bandwidth
Channel throughput is saturated!

## Slide 22: Possible Mitigation (Cont.)
Adding more channels
  Decrease individual throughput.
  Increase contention to RACH.

## Slide 23: Connecting the Dots
The concept of connection
  Data networks
    Connection unaware
    Simply forward packet for connection
  Cellular networks
    Lack of power and computation in end devices
    Page, wake and negotiate for connection
Amplifying a single incoming packet to expensive connection mechanism is the source of the attacks.

## Slide 24: Clash of Design Philosophies
Data network
  Built on the end-to-end principle.
  Applications do not expect nothing other than best effort delivery.
Cellular data network
  Still fundamentally circuit-switched systems
  Specialized to mobile devices and ensures a device is ready to receive.
Rigidity from specialized network
  Unable to adapt to meet changing requirements and conditions
  When conditions change, the rigidity causes break.
Notes: Reliable delivery, content confidentiality and in-order arrival: all responsibility of higher layer

## Slide 25: For Robust Cellular Data Network
The move to larger flow pool or shorter paging
  Mitigation possible for this work
  Eventual security?
As long as there is difference in delivering packet, exploitable mechanisms will exist.
Can we just forward packet?
  Eliminating needs for paging
    Smarter end devices
    Location-awareness
  Power problem
    Shorter sleep cycle
    More computation
Notes: There are some researches to reduce paging overhead and the mobile network is actually evolving with larger flow pool and shorter paging.

## Slide 26: Conclusion
They find two new vulnerabilities to demonstrate that low bandwidth DoS attacks can block legitimate cellular traffic.
These attacks are from not mismatch of bandwidth rather from different network topology “smart” and “dumb”.
Rigidity fails to adapt changing conditions.
Without fundamental change in cellular data network design, the low-bandwidth exploits are not easy to be solved.

## Slide 27: Questions

## Slide 28: Garbage

## Slide 29: Introduction
The interconnection of cellular networks and the Internet
  Significant expand of the services on telecommunications subscribers
New vulnerabilities from conflicting design philosophies
  Cellular networks
    Smart, controlled
  The Internet
    Dumb, best effort service
  None have examined the inherent security issues caused by the connection of two systems built on opposing design tenets.

## Slide 30: Vulnerabilities
To new vulnerabilities that can deny cellular data services and voice services.
  Exploiting Connection Teardown
  Exploiting Connection Setup
These attacks target connection teardown and setup procedures in networks implementing General Packet Radio Service (GPRS).