## Slide 1: On Cellular Botnets: Measuring the Impact of Malicious Devices on a Cellular Network Core
Patrick Traynor, Michael Lin, Machigar Ongtang, Vikhyath Rao, Trent Jaeger, Patrick McDaniel and Thomas La Porta
ACM CCS 2009
Oct. 31th, 2012
Presented by YoungGyoun Moon
# Slides are partially brought from the authors’ presentation in ACM CCS 2009.
Notes: Goal of this presentation is to go through the slides ASAP, and finish it before any of you fall asleep.
So please give me your attention and supportive reactions.

## Slide 2: Introduction
Botnet
  A set of compromised network-connected machines
Notes: First, the attacker, the red guy, who is called bot master, spreads out a malware with Trojan virus in it.
And then, if the user executes the malware without any suspicion, the machine w/o any prevention can be infected by Trojan horse virus.
After then, bot master can control the compromised machines remotely.
If black guy comes to red guy and pay some money to say “KAIST mail server sucks, please attack it!”
And then red guy can use his thousands of (or even millions of) machines to flooding ping packets or SYN packets to the mail server.
For the tremendous amount of packets coming in, the mail server could not do anything, so that any mail service would not work.
BOOM! That’s it.
This is a very typical story of botnets and DDoS attacks.

## Slide 3: Introduction
Botnet (cont.)
  Spamming
  DDoS (Distributed Denial-of-Service)
Cellular network vs. Internet network
  Centralized structure vs. Distributed structure
Let’s break down cellular network using cellular botnets!
Notes: How can we become famous? What system should we break down?
The author’s answer was ‘hey, how about cellular network’?
Cellular network is like an “air” to us nowadays.
Everyday, we makes a phone call, send SMS messages, and so on.
Even more, these days, we do kakaotalk and web serfing using 3G or 4G network.
So it is very nice and yummy target for the attackers.
Can we break down the whole cellular network?
According to these authors, the answer was “YES”.

## Slide 4: Cellular Systems
SGSN (Serving GPRS support node)
  Delivers data packets from and to the mobile stations
Notes: To understand how to do it, Let’s go a little bit deeper into the cell network.

## Slide 5: Cellular Systems
HLR (Home location register)
  Central database with each mobile phone’s information

## Slide 6: Attack Overview
GOAL : To overwhelm a specific HLR using a set of compromised phones
Attacker
Legitimate User

## Slide 7: Attack Overview
Different from DoS on Internet
  Only specific types of messages are acceptable.
  The goal is widespread outage over whole network.  Local congestion should be avoided.

## Slide 8: Attack Overview
Goal of this paper
  Find the most effective way to attack
    Determine the operations which creates biggest workload
  Estimate the required size of cellular botnets
  Find out how to avoid network bottlenecks

## Slide 9: Outline
Introduction
Attack Overview
Characterizing HLR Performance
Profiling Network Behavior
Measuring the Attack Impact
Conclusion

## Slide 10: Characterizing HLR Performance
Telecom One (TM1) Benchmarking Suite
  MQTh: Maximum Qualified Throughput
Setting:
  HLR:
    Xeon 2.3 GHz * 2 + 8 GB RAM
    Linux 2.6.22
    MySQL 5.0.45 and SolidDB 6.0

## Slide 11: Characterizing HLR Performance
Types of HLR service requests

## Slide 12: Characterizing HLR Performance
Writing operation vs. Reading operation
or doing BOTH?

## Slide 13: Characterizing HLR Performance
Types of HLR service requests

## Slide 14: Characterizing HLR Performance
HLR throughput for different requests
  500K subscribers
Expensive about 5x more

## Slide 15: Characterizing HLR Performance
Different commands vs Number of subscribers
  MySQL (Only caching data and indexes in memory)

## Slide 16: Characterizing HLR Performance
Different commands vs Number of subscribers
  SolidDB (All in memory)

## Slide 17: Characterizing HLR Performance
Bottom line
  Selecting certain subsets of requests can improve the efficiency for attack.
  More information of core network will be useful. (i.e. which DB used in HLR)

## Slide 18: Profiling Network Behavior
Measure the impact of the HLR requests on a live network.
Setting:
  Nokia 9500 with Symbian S80
  Motorola A1200 with Linux kernel 2.4.20
  Live cellular network
  AT command + 2 sec delay
    Some phones caused extended delays as immediate execution

## Slide 19: Profiling Network Behavior
Calculate how much commands per second available for following 4 commands
  GPRS Attach: update_location
  Call Waiting: update_subscriber_data
  Insert Call Forwarding: insert_call_forwarding
  Delete Call Forwarding: delete_call_forwarding

## Slide 20: (1) GPRS Attach: update_location
Caching algorithm
  Grouping 5 commands into one vector

## Slide 21: (1) GPRS Attach: update_location
Average response time from HLR (peak)
  = 3 seconds

## Slide 22: (1) GPRS Attach: update_location
Turnaround time
  3 sec response time + 2 sec command delay
  0.2 commands per second
  But, Only one of five commands reaches the HLR
  0.2 / 5 = 0.04 commands per second

## Slide 23: (2) Call Waiting: update_subscriber_data
Average response time
  2.5 seconds

## Slide 24: (3) insert_call_forwarding / (4) delete_call_forwarding
Average response time
  Insert : 2.7 sec - Delete : 2.5 sec

## Slide 25: Comparison
Turnaround time
  update_location : 0.04 commands/sec
  update_subscriber_data : 0.22 commands/sec
  insert_call_forwarding : 0.21 commands/sec
  delete_call_forwarding : 0.19 commands/sec
  Choose insert_call_forwarding

## Slide 26: Measuring the Attack Impacts
The effect of an attack on HLR (using MySQL)
  Attack traffic consists of insert_call_forwarding query
  with 1 million users

## Slide 27: Measuring the Attack Impacts
The effect of an attack on HLR (using SolidDB)
  with 1 million users

## Slide 28: Measuring the Attack Impacts
# of infected phones required to shutdown HLR
  MySQL with Normal condition
    Requires 2500 TPS of attack traffic
    = 11750 infected mobile phones (1.2% of total)
  MySQL with High traffic
    Requires 5000TPS of the attack traffic
    = 23500 infected mobile phones (2.4% of total)
  SolidDB:
    141000 infected mobile phones (14.1% of total)

## Slide 29: Avoiding Wireless Bottlenecks
Wireless portion of the cellular network

## Slide 30: Avoiding Wireless Bottlenecks
Wireless portion of the cellular network
  Possibility of congestion in two channels: RACH and SDCCH
  RACH (Random Access Channel)
    The attack would need to be distributed over α base stations:

## Slide 31: Avoiding Wireless Bottlenecks
SDDCH (Standalone Dedicated Control Channels)
Then, how to distribute and control infected phones over > 375 base stations?

## Slide 32: Command and Control
Internet Coordination
  3G / WiFi (we now have smartphones!)
Local Wireless Coordination
  Bluetooth
Indirect Local Coordination
  Via RACH
  Suggestion: use exponential back-off algorithm
    to rapidly react to channel conditions

## Slide 33: Possible Mitigations
HLR Replication
  Common way of defending DoS atttack
Use robust database system
  i.e. SolidDB than MySQL
Filtering
  i.e. When a large volume of insert_call_forwarding arrives

## Slide 34: Summary
Where to attack?  HLR (central database)
How to attack?  by flooding insert_call_forwarding
What do we need?  compromised cell phones (1.2% of total, MySQL case)
Any limitations?  local wireless bottlenecks

## Slide 35: Conclusion
Small cellular botnets can perform DoS attack on HLR to degrade all the network.
Local channel capacity in cellular network is the main obstacle to perform DoS attack.
More and more threats these days
  Security holes in smartphones
  Increased channel capacity of LTE network
Be aware of it!

## Slide 36: Thanks for Listening!