## Slide 1: Ghost Talk: Mitigating EMI Signal Injection Attacks against Analog Sensors
Denis Foo Kune, John Backes, Shane S. Clark, Daniel Kramer, Matthew Reynolds, Kevin Fu, Yongdae Kim, and Wenyuan Xu
IEEE Symposium on Security and Privacy 2013

## Slide 2: Sensing-and-Actuation System
Events
Sensor
ADC
Amp
Actuator

## Slide 3
Notes: What happens if a malicious adversary can cause this failure intentionally?
The rest of this talk will discuss how an adversary can fail sensors intentionally, which may cause fatal accidents like this.

## Slide 4: Sensor & Security
Many prevention and detection mechanisms
  For malicious network traffics
  For software vulnerabilities
IoT
Device
Network packets
Software vulnerabilities
Sensor input (or output)
  Sensor = A new attack vector
Notes: On the other hand, IoT devices blindly trust sensing inputs, and therefore, if we can manipulate sensing inputs, we can cause serious incidents as well.
So far, not many have been worried about sensor hackings and there is no good defense against it.

## Slide 5: Attack Vectors of Sensors
Three interfaces
  Sensitive to legitimate physical quantities
  Insensitive to other physical quantities
  Need to send sensor data to the system
Sensor
Legitimate channel
Non-legitimate channel
Physical
quantities
Embedded
System
Spoofing attack
Side-channel attack
Side-channel attack
Notes: The first attack is the spoofing attack on a legitimate channel. In the following video, you will see a heart beat sensor counting the number of heart beats for one minute. I’ll show that using a green laser pointer, you can spoof the number of heart beats.

## Slide 6: Heart Rate Sensor Spoofing
Notes: The heart beat sensor is designed to detect movement on your wrist using the green laser. We simply turn the green laser pointer on and off 100 times per minute. We made it to miscalculate the number of heart beats.
Like this, if an attacker understands the mechanism behind the design of a sensor, she may spoof it easily. If this does not look serious, let’s look at the next example.

## Slide 7: EMI on analog inputs
Analog
Digital

## Slide 8: Classification on EMI
 | Intensional | Unintentional
Low Power | Yet to be explored | Circuit design issue
High Power | Can disable circuits | A lot of work

## Slide 9: Voltage Induction

## Slide 10: Between Sensor and Amp?
Analog Sensor
AS
Micro- processor
AMP
ADC
Sensor
Input
Analog
Digital
On the order of few V
On the order of few mV

## Slide 11
MICROPHONE

## Slide 12: Modulated EMI Attack
Signals in high frequency range can be injected well compared to low frequency signals
Demodulation due to
  Nonlinear components
  Analog-Digital Convertor (ADC)
  Capacitor & Diode

## Slide 13: Attack technique 1: Black Box
Logitech Quickcam Ultravision
The attacker knows nothing about the target system
Cannot guess the length of a wire
Reverse tune all the frequency suspected

## Slide 14: Attack Technique 2: Gray Box
Plantronics Voyager 510
Partial information
  microphone-amplifier wire length
Can roughly guess the resonant frequency of the wire
Antenna length ≒ λ/4
  6cm wire -> 1.25GHz

## Slide 15: Attack Technique 3: White Box
MicaZ mote fitted with an sensor board
The whole schematic of the device is available
Multiple capacitors between the microphone and the amplifier
Conventional AM technique used

## Slide 16: Use case

## Slide 17
CARDIAC MEDICAL SYSTEM

## Slide 18: Inducing waveforms on EKG
EKG
Signal generator
Oscilloscope
Modulation waveform source
Patient simulator

## Slide 19: EKG – V-fib patient
Ventricular fibrillation
Induced 66 bpm signal

## Slide 20: Cardiac Implantable Devices

## Slide 21: Standard Lead Design
Anode
Cathode

## Slide 22: Application to medical devices
Modern devices amplify this region
Induced signals here could be dangerous
Notes: Malicious signal waveform can look just like the real thing.
Alternate diagram: Hayes [2008, fig 12.1]

## Slide 23: Sensing algorithm
Assuming bipolar configuration
QRS complex and detection

## Slide 24: Results
Device | Open air | Saline | SynDaver
Medtronic Adapta | 1.36m | 0.03m | Unknown
Medtronic Insync Sentry | 1.57m | 0.05m | 0.08m
Boston Scientific ICD | No response | Unknown | Unknown
St. Jude ICD | 0.76m | Unknown | Unknown

## Slide 25
Defenses

## Slide 26: Shielding

## Slide 27: Noise Cancellation with Adaptive Filter
Antenna
Adaptive FIR Filter
Adaptive Algorithm
+
x[n] + w1[n] + m[n]
m[n]
Original Signal
-m’[n]

## Slide 28: Results

## Slide 29: Sensing-and-Actuation System
Actuator
Amp
ADC
Sensor
Event
Amp
ADC
Sensor
Situation Aware Logic
PLC

## Slide 30: Questions?
Yongdae Kim
  yongdaek@kaist.ac.kr
  http://syssec.kaist.ac.kr/~yongdaek
  Facebook: https://www.facebook.com/y0ngdaek
  Twitter: https://twitter.com/yongdaek