## Slide 1: Embedded Device Analysis for Security Research
2016. 09. 27.
System Security Lab.
EE515/IS523, Security 101: Think Like an Adversary

## Slide 2: Embedded Devices
“Embedded device” from Wikipedia
“Embedded devices” as security research objects
  Every electric devices except desktops and laptops
  Usually connected to networks

## Slide 3: What’s Difference?
 | Embedded device | Personal computer
Purpose | Specific purpose | General purpose
Operating system | Various (no OS, Linux, VX Works…) | (mostly) Windows
Architecture | Various (ARM, PowerPC, AVR, 8051…) | (mostly) Intel x86
User interface | Poor (limited input and output) | Rich (monitor, keyboard, mouse…)
Static analysis object | Firmware files, ROM image, flash image… | Application files, system files
Dynamic analysis | Hard (not even possible) | Easy (Olly dbg, Win dbg, GDB…)
Hardware analysis | Required (to extract something) | Not required

## Slide 4: An Approach for Embedded Device Analysis
Hardware analysis
Firmware analysis (Static)
Extracting firmware
Public info.
(e.g., googling, datasheet)
Using info.
Access to interface (Dynamic)
Finding interfaces
Vulnerabilities
Existing works
(e.g., CVE, conference, etc.)
Proof of Concept (PoC)
Attack scenarios
Gathering information
Finding vulnerabilities
Creating exploit
Today’s topic

## Slide 5: Preparing for embedded device analysis
Step 0 ~ 3

## Slide 6: You’ve Got an Embedded Device
With LOVE…
I need zero-day vulnerabilities IN A SEMESTER.

## Slide 7: Step 0: The Beginning
Tear down
(not always reversible)

## Slide 8: Step 0: The Beginning
Tear down
Read user manuals & check normal functions (just observe & log some outputs)
Then, tear down “carefully”
https://www.ifixit.com/Teardown
(e.g., film cables)

## Slide 9: Step 1

## Slide 10: Step 1: Hardware Interfaces
Goal: Extracting useful data
(texts, interfaces, etc.)

## Slide 11: Step 1: Hardware Interfaces
Parallel communication
  LPT (Line Printer Terminal) parallel port
Serial communication
  Ethernet
  UART
  I2C
  SPI
  JTAG

## Slide 12: Step 1: Hardware Interfaces
UART (Universal Asynchronous Receiver/Transmitter)
  6 pins = VCC, TX, RX, GND, (CTS, RTS)
  (optional) Flow control using CTS (Clear To Send) & RTS (Ready To Send)
  1:1 communication
  Baud rate = usually 9600 or 115200
  For RS-232, RS-422, RS-485, etc.
  Tools: Putty, PySerial, etc.

## Slide 13: NOTE: GND
Ground or Earth or Common
  The reference voltage in “an” electrical circuit (not 0V!!)
  A relative (not absolute) concept
  Proper GND for wired communications
Where is
the ground?
10V
Load
5V
Batt.
5V
Batt.
GND symbols

## Slide 14: NOTE: GND for Comm.
10V
Load
5V
Batt.
5V
Batt.
10V
Load
5V
Batt.
5V
Batt.
Communication
processor
Communication
processor
5V
-5V
GND
GND
5V
10V
HIGH = 5V
LOW = -5V
HIGH = 10V
LOW = 0V
Cannot
communicate

## Slide 15: Step 1: Hardware Interfaces
I2C or IIC (Inter Integrated Circuit, Two-Wire Interface)
  4 pins = VCC, SDA (Serial Data), SCL (Serial Clock), GND
  Multi-master/slave bus (made by Philips Semi.)
  Among digital chips on the same board (e.g., MPU & EEPROM)
  Protocol (http://i2c.info/i2c-bus-specification)
  Tools: Arduino with “wire” library
Up to 128 slaves
Pull-up resistors

## Slide 16: NOTE: Pull-Up/Down Resistor
PIN status
  HIGH = VCC
  LOW = GND
  Floating = Undefined (i.e., opened)

## Slide 17: Step 1: Hardware Interfaces
SPI (Serial Peripheral Interface)
  6 pins = VCC, SCLK, MOSI (Master Out/Slave In), MISO (Master In/Slave Out), SS (Slave Select), GND
  Four-wire serial bus (made by Motorola)
  1:n communication using SS
  For fusing firmware, etc.
  Tools: commercial SPI programmer, Arduino with “SPI” library

## Slide 18: NOTE: Mounting Type
DIP (Dual In-line Packages)
SMD or SMT (Surface Mount Devices/Technology)
BGA (Ball Grid Array)

## Slide 19: Step 1: Hardware Interfaces
JTAG (Joint Test Action Group)
  8 pins = VCC, TMS (Test Mode Select), TCLK (Test Clock), TDO (Test Data Out), TDI (Test Data IN), TRST (Test Reset), RESET, GND
  For debugging and flashing firmware
  Tools: commercial JTAG debuggers

## Slide 20: Step 2

## Slide 21
WM9715
Audio and
Touchpanel CODEC
Samsung S3C6410
ARM1176 Processor
SPANSION
NAND Flash
Memory (4G)
Samsung K4X1G323PE
1G DDR RAM
TI MAX3243
3V-to-5V RS232 Line Driver
TI TL16C2550
1.8V-to-5V Dual UART
TOSHIBA TLP291-4
Programmable Controller
DAVICOM DM9000BI
Ethernet Controller
Sipex SP232E
RS232 Line Driver
TI MAX3232
3V-to-5V RS232
Line Driver
???
A company’s device

## Slide 22: Step 2: Access to HW Interface
Datasheet (e.g., TI MAX3232 RS-232 Line Driver)
  Features
  Pin map/assignment/configuration
  Pin description
  Application schematic or layout example

## Slide 23: Step 2: Access to HW Interface
Tracing PCB routing (using your eyes or multi-meter)
Letters and figures = silk layer
GND
(by copper pour)

## Slide 24: NOTE: PCB
PCB (Printed Circuit Board)
PCB artwork
Letters and figures = silk layer

## Slide 25: NOTE: PCB
PCB (Printed Circuit Board)
Smart phone

## Slide 26: Step 2: Access to HW Interface
Physical access
Using connectors
Soldering
Be careful…

## Slide 27: Step 2: Access to HW Interface
Logical access
  Using test tools (Jtagulator or JTAG finder)
  Or just connect, and observe until…
  Can be disabled temporarily or permanently 
  Can be disabled by software or hardware 
Jtagulator
JTAG Finder

## Slide 28: Step 2: Access to HW Interface
UART
  Booting message (CPU and memory info.)
  Bootloader access
  Shell with or without login
I2C: memory read/write
SPI: memory read/write
JTAG: dynamic debugging, memory read/write, etc.
A company’s device

## Slide 29: Step 2: Access to HW Interface
Download on the Internet (previous model or series)
Firmware extraction
  Through external storage (USB, SD-Card, etc.)
  Useful tools in the original system
    ftp(d), tftp(d), netcat or nc, telnet(d), etc. ( “/bin/busybox”)
  Cross-compile some tools & put them in the target system
  Memory dump

## Slide 30: Step 2.5: Direct Access
Flash memory dump
  Soldering jumper cables on the PCB
  De-soldering (chip off) using soldering irons or rework station
Rework Station

## Slide 31: Step 2.5: Direct Access
Ex) Samsung NAND flash memory on “a” device
  Using a programmable MPU module (commercial AVR module, Arduino Mega, Bus pirate, etc.)
K9F1208U0C
Memory socket
Memory socket

## Slide 32: Step 2.5: Direct Access
PIN name | PIN description
I/O0~7 | DATA INPUTS/OUTPUTS
CLE | COMMAND LATCH ENABLE
ALE | ADDRESS LATCH ENABLE
CE/ | CHIP ENABLE
RE/ | READ ENABLE
WE/ | WRITE ENABLE
R/B/ | READY/BUSY OUTPUT
Read ID operation (0x90 command)
Implement this !!

## Slide 33: Step 3

## Slide 34
Extracted binary
Packed or compressed
Encrypted
Unknown (customized)
Extracted file system
No
Yes
IDA Pro?
Yes
Yes
Hex-Rays?
No
Decrypt?
Googling?
No
No
File system?
Yes
Yes
No
But, every binary is different…
(architectures, devices, manufactures, standards, etc.)
* or ???

## Slide 35: Step 3: Basic Firmware Analysis
Automatic analysis (using tools)
  Binwalk
  Firmware Modification Kit (FMK)
Manual analysis (using your brain and luck)
  Finding patterns or signatures
Binwalk example
(B company’s device)

## Slide 36: Step 3: Basic Firmware Analysis
Manual analysis example
  C company’s firmware = single BIN file
Header size
File size
File sequence
number
Repeated pattern

## Slide 37: Step 3: Basic Firmware Analysis
13 images
  Three Yaffs (Yet Another Flash File System) images (VMS Alpha executable)
  One CD-ROM image and others

## Slide 38: Step 3: Basic Firmware Analysis
Yaffs image file
File content
Filename

## Slide 39: Step 3: Basic Firmware Analysis
Pattern
  16 byte data per every “0x800” byte
  Page header
    Always 0x00001000 (4 byte)
    Object ID (4 bytes)
    Page sequence number (4 bytes)
    Page length (4 bytes)

## Slide 40: Step 3: Basic Firmware Analysis
Basic check list
  Strings (readable info. for human)
    Useful messages or numbers, hardcoded ID/PW, and hidden commands…
  Booting sequences
    Init.d, rcS, and shell scripts running in booting sequences…
  External interfaces
    Socket (parameters), bind (port), and listen (status)…
    External USB memory, SD-Card…
  Updates
    Fixed IP addresses, URL or PATH
    Configurable conditions for updating
  ETC.

## Slide 41: Good Luck to Your Projects

## Slide 42: How About Wireless Spoofing

## Slide 43
Q&A