## Slide 1
Security Analysis of the
Diebold AccuVote-TS Voting Machine
EVT '07
A. Feldman, J. Halderman, and E. Felten
Presenter
Donghwan Kwon
This file is originally written by Dawon Park,
Revised by Donghwan Kwon
Notes: Usenix Electronic Voting Technology workshop 2007

## Slide 2
Party |  | % | Vote
 | Democratic | 52.3 | 42,338,795
 | Republican | 44.3 | 35,857,334
United States elections, Nov 2006
Notes: 올해 5월 대선 투표. 국민의 관심.
때론 결과에 대한 의혹. 투표가 조작되었는가? 조작될 수 있는가? 심각한 문제
리뷰할 논문은 2006년 11월 미국에서 사용될 전자 투표기의 해킹 가능성에 대한 내용.
Release 날짜는 2006년 9월. 두달 뒤, 이 기기를 이용한 선거 예정
385개 시, 10%의 유권자들이 사용예정

## Slide 3
Voting
Electronic
Voting
Paper-based
Voting

## Slide 4
AccuVote-TS Voting Machine
Direct Recording Electronic
(DRE)
Windows CE
Software
Software
Notes: //2//
왜 AccuVote-TS? 논란의 중심, 2006년 11월 미국 385개 시, 10%의 유권자들이 사용예정
논문 릴리즈 Sept. 13, 2006
DRE – 선거 소프트웨어를 돌리기 위한 일반적인 컴퓨터
Windows CE – embedded 장비를 위한 일반적인 OS

## Slide 5
AccuVote-TS Voting Machine
Notes: //3//
F - Boot device 순서
E – EBROM
G – Flash Memory card
C – On-board flash memory chips
J – smart card reader

## Slide 6
AccuVote-TS Voting Machine
MODE
Pre-Download
Pre-Election
Election
Post-Election
Download a list of
races and candidates
GEMS server software
Logic and Accuracy testing
Checking tally is correct.
Voter access card
(valid -> invalid)
On-board Flash memory,
Flash memory card
accumulator
mode
memory
card
Local network
Phone line
Serial cable
Local network
Accumulator mode
Notes: //4//

## Slide 7
Attacker’s Goal
Vote Stealing
Denial of Service
Party |  | % | Vote
 | Democratic | 52.3 | 42,338,795
 | Republican | 44.3 | 35,857,334
5% (4,048,777)
Party |  | % | Vote
 | Democratic | 47.3 | 38,290,018
 | Republican | 49.3 | 39,906,111
Party |  | % | Vote
 | Republican | 49.3 | 39,906,111
 | Democratic | 47.3 | 38,290,018
Notes: //5//
지지 후보 최소 득표 수 보장
증거는 남지 않는다 (총 투표수 유지, 로그 삭제)
Secret knock
특정 시간, 지역의 기계 고장
비정상적인 숫자로 바꾸기
Sleep mode

## Slide 8
Attacker’s Goal
Notes: 득표 조작 성공 데모
http://citp.princeton.edu/research/voting/videos/
이 논문에는 evaluation 없음

## Slide 9
Vulnerability
Easy to physically access to the motherboard
- EPROM chip, removable memory card, power button
Source of bootloader code is changeable
- EPROM chip / Flash memory / On-board flash memory
Not verify authenticity of files
- fboot.nb0, nk.bin, EraseFFX.bsq explorer.glb, .ins file
Spreading Virus
Direct Installation
Removable memory card can spread out virus
- Used for multiple machine, rewritable memory
Notes: //8//EPROM 변경 – several screws, side locked door key – 10초 or 카피 구하기 쉬움(일반 가구나 주크박스, 호텔 미니 바에 많이 쓰는 열쇠)
Record encryption key is stored in machine’s memory
메모리카드는 여러 번 이동한다. (Pre, Post election, software upgrade)
악성 Bootloader 는 메모리카드에 악성 코드를 옮긴다.

## Slide 10
Attack Scenario – installing malware
① Replace EPROM chip
  Create EPROM chip
  Open the machine
  Install it, and reboot
Determine source of bootloader code
② Insert Memory Card
Notes: //9//페이퍼에는 1. EPROM chip 만든다 2. 머신을 연다 3. 마더보드에 설치하고 재부팅한다.
악성코드 from EPROM -> flash memory

## Slide 11
Attack Scenario – installing malware
Notes: 페이퍼에는 1. EPROM chip 만든다 2. 머신을 연다 3. 마더보드에 설치하고 재부팅한다.
Several screws

## Slide 12
Bootloader copies itself to RAM
Look for memory card in PC slot
Fboot.nb0
Exist?
Bootloader in
On-board flash
Copies fboot.nb0 to
On-board flash
Y
Nk.bin
Exist?
Replace OS image on
On-board flash
Y
EraseFFX.bsq
Exist?
Erase entire file system area of flash
Y
Does not verify
authenticity
of these files
N
N
N
Cont.
Attack Scenario – installing malware
Notes: /12/우리나라 임베디드 기기도 파일명만 체크하는 경우가 많음. -> 일반적!

## Slide 13
Uncompress OS in
On-board flash,
copy to RAM
Cont.
Jump to OS kernel
Runs Filesys.exe
Runs
Shell.exe
Device.exe
Gwes.exe
Taskman.exe
Run BallotStation
(Voting software)
Portable Flash
Exist?
Y
Invoke
Windows Explorer
N
Explore.glb
Exist?
.ins file
Exist?
Y
Automate update
Mounting file system
On-board flash : \FFX
Portable flash: \StorageCard
RAM(root): \
Accept without any authentication
Attack Scenario – installing malware
Y
Notes: \StorageCard\CurrentElection\election.brs (투표 결과)
\FFX\AccuVote-Ts\BallotStation\Currentelection\election.brs (투표 결과 백업)

## Slide 14
Suspend
BallotStation
Open
Result file
Election mode?
Y
Select Candidate
New Ballot?
Rigged race?
Steal Vote
Resume
BallotStation
Y
Y
N
N
N
15sec
Attack Scenario – stealing vote
Insert a Memory Card
Notes: //15//목적: 조작 + 은닉
\StorageCard\CurrentElection\election.brs (투표 결과)
\FFX\AccuVote-Ts\BallotStation\Currentelection\election.brs (투표 결과 백업)
계속 돌면서 투표결과 파일과 백업 파일 변경
은닉 : 시크릿 노크, 등등

## Slide 15
Mitigation
S/W & H/W modification
- Code signing & signature verification
- Person confirm for software updates
- Not use rewritable storage -> tamper-proof logs, records
Enhance physical access control
Parallel testing
Effective certification system
Software independent design
Notes: //16// Chain of custody 관리연속성. During the transfer of Memory Cards
Parallel testing -> For detection
Software independent design – Voter-verifiable paper audit trail

## Slide 16
Conclusion
H/W & S/W encompassing study of a widely used DRE
Demonstration of vote-stealing and virus spreading
Warning for large scale fraud
Proving H/W architecture limitation of the target
Notes: //18/

## Slide 17
Limitation & Future work
General attack idea -> Attack through network
Physical access is not so easy during voting
Notes: //19//

## Slide 18
`03
Kohno et al.
- Numerous security flaws in software.
`03
Maryland
SAIC “High risk of compromise”
RABA, confirmed Kohno’s findings.
`03
Ohio, Compuware
- DRE systems high-risk security problems.
“None of them offered the public a detailed technical description.”
`06
Harri Hursti
Hardware & compiled boot-loader
Problems with software update
`06
Feldman, Halderman, Felten
Reverse engineer hardware & software
Confirmed earlier studies by demo
`02
Another Story – Diebold
Notes: //21//1859설립. 지금 전세계 ATM 35%
2002, Globcal election syste을 $24.7 million (250억원)에 사면서 Diebold Election system 이름으로 미국 투표 업계에 들어옴.
2003, 타다요시 코노 논문 – 최소한의 보안 수준, 그 이하다. (YDK: Diebold's anonymous ftp site. 논문 추가정보)
Harri Hursti, 하드웨어를 가지고 연구할 기회!
2009년 이름 바꿈.

## Slide 19
`07
David Wagner, California
TTBR(Top to Bottom Review)
“Deep architectural flaws”
Buffer overflow, weak cryptography
`07
Ohio
Project EVEREST
“Yet more vulnerabilities”
Election Systems & Software
인수
`09
Dominion Voting System
인수
`10
Another Story – Diebold
Notes: //23//이후에 정부에 $2.6 million 소송(26억원), 인증취소
`08년에는 Diebold 전체를 $2.63 billion (2조)에 팔라는 제안도 있었음 (03년 처음 사업시작할때쯤 매출이 $2.1 billion (2조))
`09년에 사업부 매각 ( $ 5 million (50억원), 살때는 24.7 million)
Lession! 어떻게 보면 기술적으로 가치가 낮은 논문. But 민주주의를 지탱하는 선거에 영향을 줌. 민주주의를 지키기 위한 리서처

## Slide 20
Electronic voting in Korea
Secure?

## Slide 21
Thanks