## Slide 1: DolphinAttack: Inaudible Voice Commands
Guoming Zhang, Chen Yan, Xiaoyu Ji, Tianchen Zhang, Taimin, Zhang and Wenyuan Xu
Zhejiang University
Presenter : Hojoon Yang

## Slide 3
Today:
“Okay google, Text YDK I’m going on vacation tomorrow”
“Okay google, Call YDK”
“Okay google, Open Gmail”
“Okay google, Go to security101.kr”
“Okay google, Set alarm for 10 a.m.”
…

## Slide 4
In the near future?
“Okay google, pay hojoon $100”
“Okay google, open the door”
“Okay google, unlock the car”
“Okay google, start the car”
“Okay google, set my home temperature at 60 degree”
…

## Slide 5
Voice channel opens up new possibilities for attack
Is voice more secure than fingerprint? Is current implementation of voice recognition secure?

## Slide 6: Threat model
What should I do?
?
“.....”

## Slide 7: 1. Audible and Intelligible
“Okay Google!”

## Slide 8: 1. Audible and Intelligible
“Okay Google!”
“Okay Google??”

## Slide 9: 2. Audible But Not Intelligible
Can you play dollhouse with me and get me a dollhouse?

## Slide 10: 2. Audible But Not Intelligible
“Cocaine Noodle!”

## Slide 11: 2. Audible But Not Intelligible
“Cocaine Noodle!”
“Cocaine noodle….?”
“Cocaine Noodle = Okay Google”

## Slide 12: 2. Audible But Not Intelligible
“*%$&@*$&@*##”

## Slide 13: 2. Audible But Not Intelligible
“*%$&@*$&@*##”
“hmm..”

## Slide 14
Command 1 : “Okay google”
Command 2 : “Okay google, Open xkcd.com”

## Slide 15: 3. In-Audible
“Okay Google!”

## Slide 16: 3. In-Audible
“Okay Google!”
“…..”

## Slide 17: Related work
Cocaine Noodles: Exploiting the Gap between Human and Machine Speech Recognition, USENIX WOOT 2015
Hidden Voice Commands, USENIX 2016
 | Human intelligible? | Machine Intelligible? | Works well?
Audible Voice command | Yes | Yes | 
Audible Voice command | No | Yes | 
In-Audible Voice command | No | Yes | 

## Slide 18: Background
ADC
Microphone
Amplifier
Low Pass Filter
Voice signal
Voice Recognition System
Voice Capture System

## Slide 19: Background
ADC
Microphone
Amplifier
Low Pass Filter
Voice signal
Human voice is baseband signal which is
2k
0
Voice Capture System

## Slide 20: Background
Modulation
2k
0
24k
0
26k
22k

## Slide 21: Background
ADC
Microphone
Amplifier
Low Pass Filter
Modulated voice signal
24k
0
26k
22k
Hmm…Its impossible.
Cocaine noodle Author
Voice Capture System

## Slide 22
Hmm…Its impossible.
Cocaine noodle Author
DolphinAttack Author
But… It works!
Previous work [61] considers it impossible to receive voices above 20 kHz.
Since most speech recognition systems apply band-stop filters to attenuate signals that fall outside of the range of human speech and require a minimum power level for parsing speech, the adversary does not attempt to construct a covert audio channel that cannot be perceived by the human ear.
DolphinAttack

## Slide 23: Background
ADC
Microphone
Amplifier
Low Pass Filter
Modulated voice signal
24k
0
26k
22k
Cocaine noodle Author
Voice Capture System

## Slide 24: Non-linearity
ADC
Microphone
Amplifier
Low Pass Filter
Voice signal
Voice Capture System

## Slide 25: Non-linearity
ADC
Microphone
Low Pass Filter
Voice signal
Nonlinearity term

## Slide 26: Non-linearity
ADC
Microphone
Low Pass Filter
voice signal
Voice Recognition System

## Slide 27: Non-linearity
ADC
Microphone
Amplifier
Low Pass Filter
Modulated voice signal
Voice Capture System

## Slide 28: Non-linearity
ADC
Microphone
Low Pass Filter
Modulated voice signal
Does it really work?
Voice Recognition System
Voice signal
The received SPL for the ultrasound is measured at
10 cm away from the Vifa [9] speaker and is 125 dB.

## Slide 29: Can you distinguish?
vs
원본
Nonlinear term

## Slide 30
Are we done?
No, we have an authentication problem

## Slide 31: Siri knows who the owner is
User-dependent activation
Siri does not be activated by the non-owner voice.
Even in-audible voice is not much different.
ANY SOLUTION?

## Slide 32: Solution #1
Brute force
  Device is trained by Google TTS engine.

## Slide 33: Solution #2
Concatenative Synthesis
  When an attacker recorded owner’s sentences except “Hey Siri”
ㅎㅣ
ㅋㅔ이크
헤이

## Slide 34
Evaluation

## Slide 35: Hardware defense #1
Modulated voice signal
Voice Recognition System
ADC
Microphone
Amplifier
Low Pass Filter
Voice Capture System
Low Pass Filter

## Slide 36: Hardware defense #2
Voice Recognition System
ADC
Microphone
Amplifier
Low Pass Filter
Voice Capture System
X
Modulated voice signal

## Slide 37: Software defense
Original
Recorded
Recovered

## Slide 38: Conclusion
Authors find …
  Inaudible voice attack is possible.
    Amplitude Modulation
    Nonlinear component
Do Not Trust The Paper TOO MUCH. Be critical.

## Slide 39: Limitation and Future work
Poor defense.
  Starbucks siren order
Authentication solution is non-sense.
Attack distance is not very long.(max. 1m)
Attack needs high power signal.
Attack can be exposed by device response